## Slide 1: Maintenance Asset Health Index
Rene J. Nazario-Diaz
CEO

## Slide 2: Maintenance Asset Health Index

## Slide 3: Challenge: Making the connection
Maintenance Transactional Data
Vital Signs
Asset Health?
Asset Risk?

## Slide 4: Use what we have at hand
Work Orders
Overhauls
Asset Criticality
Asset Condition Assessments
PM/CM History
MRO Usage/ Inventory
Notes: MAHI by Sub-system detail is a combination of:
  Asset Condition
  WO Split
  Overhaul
  Inventory Compliance
  PM Compliance
  WO Priority

## Slide 5: Use what we have at hand
Notes: MAHI by Sub-system detail is a combination of:
  Asset Condition
  WO Split
  Overhaul
  Inventory Compliance
  PM Compliance
  WO Priority

## Slide 6: MAHI for Combined-cycle gas-fired Power Plant (Steam Turbine)
Transformer AHI
Generator AHI
Steam Turbine AHI
Control AHI
BOP AHI
HRSG AHI

## Slide 7: Maintenance Asset Health Index
Probability – How much time left before the next major overhaul? How much risk?
PM Compliance – Are we keeping up with our PM Program? Generate all WO’s. Complete all WO’s (on-time)
WO Split (Preventive/Corrective) – How effective is my PM Program? If we’re doing our PM’s right, we should have fewer corrective actions.
WO Priority – Are we taking care of the highest priority Work?
Asset Condition – What is the condition of the asset according to the people on the field?
Critical Spares – Do I have the right spares in the right quantities when needed?

## Slide 8: Maintenance Asset Health Index
Probability, Risk, Time
Last Major Overhaul
Next Major Overhaul
months
Feb 2018
Feb 2021
(36 months)
months
Feb 2020 (24 months)
Gas turbine
24/36 = 66%
Gas turbine overhaul

## Slide 9: Maintenance Asset Health Index
Preventive Maintenance (PM) Schedule Compliance
Last Major Overhaul
Next Major Overhaul
months
Scheduled End Date = Actual End Date (HIT)
PM Schedule
WO Generated
WO Closed (on-time)

## Slide 10: Maintenance Asset Health Index
Work Order Split
Last Major Overhaul
Next Major Overhaul
months
Corrective WO’s
Preventive WO’s

## Slide 11: Maintenance Asset Health Index
Work Order Priority = Asset Criticality * WO Impact * WO Age
Last Major Overhaul
Next Major Overhaul
months
Urgent WO’s
Priority 1
Priority 2
Priority 3

## Slide 12: Maintenance Asset Health Index
Criticality Code | Description
1 | Does NOT affect Operation
2 | NON-Essential to Operation - Backup Available
3 | NON-Essential to Operation - No Backup Available
4 | Essential to Operation - Backup Available
5 | Essential to Operation - No Backup Available
6 | Essential to SAFETY
WO Impact | Description
1 | Routine Checks and less important tests
2 | Operational test/Performance verification
3 | Preventative Maintenance/Inspection
4 | To improve performance and/or reliability
5 | Defect affects performance of main Equipment
6 | Fault Caused an OUTAGE, Elimination necessary
7 | Fault Endangers Vital Equipment
8 | Elimination of Fault is indispensable to SAFETY
Work Order Age (days) | Work Order Age (weeks) | Weight
0-14 | 1-2 | 1
15-30 | 3-4 | 2
31-45 | 5-7 | 3
46-60 | 8-9 | 4
61+ | 10+ | 5
Age Factor

## Slide 13: Maintenance Asset Health Index
Calculated Priority = Asset Criticality Factor * WO Impact Factor * Age Factor
If Calculated Priority is between 1 and 9, then Priority = "Priority3"
If Calculated Priority is between 10 and 18, then Priority = "Priority2"
If Calculated Priority is between 19 and 29, then Priority = "Priority1"
If Calculated Priority is Greater than 30, then Priority = "Urgent"

## Slide 14: Maintenance Asset Health Index
Age Weight factor = 1
Age Weight factor = 2
Age Weight factor = 3
Age Weight factor = 4

## Slide 15: Maintenance Asset Health Index
Asset condition (snapshot)
) x100
Asset
Criticality
Work Order
Condition Assessment
Unit 1
Gas Turbine
1st Stage
2nd Stage
Blades
Blades
Critical, Poor
Critical, Good
Condition = Poor
Critical Condition Index - Worst case scenario, based on the most critical asset in the system (Ex. If most critical asset in the system is a 6 then Max Poor Condition Factor = 30).
Critical Condition Score - CONDITION X CRITICALITY - for each of the assets in the subsystem.

## Slide 16: Maintenance Asset Health Index
Code | Condition | Comments
1 | Very Good | Only normal maintenance required
2 | Minor Defect only | Minor maintenance required
3 | Maintenance Required to return to accepted level | Significant maintenance required
4 | Required renewal | Significant renewal/upgrade required
5 | Unserviceable | asset requires replacement
0 | To be evaluated | If an asset has not been serviced in the number of months, defined for its class, the condition will be set to 0 automatically. The condition index will be an average of the work orders at closing. The original asset load will have all assets, set to Condition 0.

## Slide 17: Maintenance Asset Health Index
Critical Spares (snapshot)
Asset
Critical Spares
Critical Spares = 50%
Part ID | Quantity Required | Current Stock Level | Compliant (Hit/Miss)
ABC123 | 2 | 0 | 0 (miss)
XYZ456 | 4 | 10 | 1 (hit)

## Slide 18: Maintenance Asset Health Index
 | Probability (time consumed) | PM Compliance | WO Split | WO Priority | Asset Condition | Critical Spares | Asset Health Index (AHI)
Score | 20% | 95% | 84% | 95% | 100% | 95% | 
Weight | 5% | 20% | 15% | 15% | 35% | 10% | 
Rating | 1% | 19% | 12.54% | 14.25% | 35% | 9.50% | 91%
Here’s a little math…..
Rating = Score X Weight
Σ Ratings = AHI

## Slide 19: Maintenance Asset Health Index

## Slide 20: MAHI for predictive maintenance?

## Slide 21: MAHI for predictive maintenance?
Initial Inspections and AHI Calculation. Field crews inspect poles and EAM calculates AHI score. Assets are categorized into different health zones (Good, Fair, Poor).
Tracking and Analyzing AHI Trends Over Time. AHI scores are logged monthly/annually, identifying trends of deterioration. A pole with an AHI score declining from 4.5 to 3.2 in two years indicates a potential failure in the near future.
Apply Predictive Analytics. Predictive algorithms analyze AHI trends along with environmental and operational data. A maintenance schedule is adjusted based on projected failure risks
Preventive and Predictive Actions. Field crews focus efforts on assets showing the steepest decline in AHI scores. Assets are proactively replaced or rehabilitated before failure occurs.
Prioritize Maintenance: Focus on assets with rapidly declining AHI scores

## Slide 22
October 15th & 16th, 2025
Puerto Rico
More information coming soon! karla.cruz@visualk.com

## Slide 23: Maintenance Asset Health Index
Rene J. Nazario-Diaz
CEO